## Slide 1: Collaborative Manipulation Pipeline
Outline
  Overview
  Implementation details
  Current demonstrations
  Pros and Cons
  Next steps

## Slide 2: SBPL Demo Framework Motivation and Design Goals
Current State:
  Demos are time consuming and have to be made from scratch
  Past demos largely cannot be recreated or reused
Design Goals:
To enable multi-robot manipulation tasks (quadcopter projects out of scope)
Allow researchers to quickly script demos that feature their area of interest
Maintain demonstration code that can be reused
Allow independent development on robots on differing platforms

## Slide 3: ROS Architecture
PR2 Local Master
Actions:
  Move_base
  Move_arm
  Torso_controller
  Point_head
  TF_lookup
  Gripper Cmds
Topics:
  Raw sensor data
Rocon Hub (Redis Server)
@Dagobah:6830
Alan1
Groovy
Dagobah
Indigo
Commander Local Master
  Action clients
  Service calls
  Read topics
  Runs State Machine
  TF bookkeeping between robots
SBPL LAN
Rocon Gateway
roslaunch sbpl_multimaster alan1_gateway.launch
roslaunch sbpl_multimaster dagobah_gateway.launch
roslaunch sbpl_multimaster sbpl_hub.launch
Rocon Gateway
Roman
Indigo
Tatooine
Indigo
Groovy  Indigo Moveit Interface

## Slide 4
Move_base
Move_base SBPL (TODO)
Move_arm OMPL
Move_arm SBPL (TODO)
Point_head action
Kinect
AR Tag Detection
Gripper Actions
Move_arm SBPL
Asus Xtion + Tilt servo
No Navigation
PointGrey BlackFly
(unused)

## Slide 5: Implementation details
Sbpl_demos
ROS package to contain python-based scripting utilities
  Robot-specific action clients and services
  State machine (python based)
  AR Tag functions
Status:
  Functional, continued development
  https://github.com/sbpl/sbpl_demos
SBPL_multimaster
ROS package to manage the Rocon setup within lab
  Rocon configuration generator
  Gateway launch files
  Rocon hub launch
Status:
  Completed
  https://github.com/sbpl/sbpl_multimaster
Groovy_indigo_moveit_
wrapper
ROS package to manage PR2 from Indigo Moveit
  Custom message packages that match Groovy MD5sums
  I2g_follow_joint_trajectory action server
Status:
  Completed
  https://github.com/abrinkmacmu/groovy_indigo_moveit_wrapper

## Slide 6: Sbpl_demos
-Example usage code, not clean but may help users
-
-
Convention for finding python scripts “from sbpl_demos.pr2_helpers import GripperCommander”
- Lab maps
- Installation instructions
- Pr2 and Roman details

## Slide 7: Screen Configurations
Alan1
Groovy
Dagobah
Indigo
Roman
Indigo
Tatooine
Indigo
One Screen config per machine Aids startup time and guides users to correct launches and scripts
Contained in spbl_demos/screen_configs

## Slide 8: Sbpl_multimaster
The user should only have to modify one file
  Modify config/gateway_topics.yaml to suit your needs
  Launch the generate_multimaster_configs.yaml to create <machine>_gateway.launch files for all machines in the network
  Push the changes to the other machines
  Rerun the <machine>_gateway.launch files
Does require manual configuration of each machine after change
  could be addressed by installing workspaces
Config/gateway_topics.yaml

## Slide 9: Single Robot: Roman Demo sbpl_demos/scripts/single_robot_demos
Use AR pose detection to command a simple sequence of Arm motions
Required:
  Roman and Commander (Dagobah)
  AR Tagged item
Instructions:
  Place AR tag in view of the Asus, confirm AR pose estimation in Rviz
  The pre-grasp and post grasp are computed on the right side of the tag, so ensure the Roman can reasonably reach the tag
  Once supporting servers are running, execute roman_grasp_test.py
Improvement Ideas:
  Instead of just one grasp approach to the AR item, consider many (top down, 90 deg intervals, or RPY randomization
  Include collision object for picking surface and attached collision object

## Slide 10: Multi Robot: Hardcoded handoff sbpl_demos/scripts/multi_robot_demos
Use AR pose detection to command a simple sequence of coordinated arm motions across 2 robots
Required:
  Roman and Commander (Dagobah)
  PR2 and Commander (Tatooine)
  AR Tagged item
Instructions:
  Place AR tag in view of the Asus, confirm AR pose estimation in Rviz
  The pre-grasp and post grasp are computed on the right side of the tag, so ensure the Roman can reasonably reach the tag
  Once supporting servers are running, execute roman_pr2_hardcoded_handoff.py
Improvement Ideas:
  Coordinate collision objects between robots

## Slide 11: Pain Points Strengths
  Roman elmo/ethercat driver initialization (ongoing)
    Unhelpful error message:
      *** ERROR (12) : Erroroneous response when reading SO
    System restarts have been the only way I know to clear this issue, sometimes many times
  Rocon networking (intermittent)
    Most of the time it functions properly but occasionally subscribed topics do not appear
    Number of subscribers do not increase over the network, so beware of code that requires >= 1 subscriber to begin
  System Complexity (solved)
    Shear number of computers and electronics to manage adds significant non-value overhead
    Computers total: 9 (5 – roman, 4 – PR2), LAN configuration, Roman electronics
Rocon Solves Groovy/Indigo problem
  Barrier to entry should be low for PR2 development
Pr2 Navigation, actions, and Arm Planning
Roman Arm Planning
Lab network is robust across Pr2 and Roman
AR tag pose estimation is robust

## Slide 12: Next Steps
Demos
  Exploit more of the PR2’s features in multi-robot demo (Alex)
  Pass objects back and forth between robots indefinitely (Alex)
Features
  Explore moveit sensor manager for real-time collision obstacle generation (Tae-hyung)
  Improve arbitrarily located AR tag grasping (Alex)
  Collision object sharing between robots (Alex)
  Other-robot collision modelling (Alex)
  Get SBPL arm planner packages in sbpl_demos setup configurations (Sung)
MRSD Handoff Development
  An MRSD team of 5 people will be taking this system to create a more robust handoff system